An Energy- Efficient User Centric Approach High Capacity SG Heterogeneous Cellular  Networks

Abstract

While the concept of ultra-dense small cell networks (SCNs) has brought a number of significant opportunities for the telecommunication industry, it has also introduced a major challenge for researchers, who must develop techniques to reduce the sharp increase in power consumption that will be required to backhaul traffic from SCNs to the core network. In this research, we investigate the green backhauling challenge for a fifth generation (5G) wireless communication network that uses both the passive optical network (PON) and millimeter wave (mmWave) backhauling to support its diverse groups of customers and applications. Our approach is based on the fact that the energy efficiency figures for the PON and the mmWave technologies are different under a given load condition. The PON technology is more energy efficient under heavy load conditions, whereas the mmWave technology offers better energy efficiency under low load conditions. As such, in response to varying traffic loads during various hours of the day, a fixed backhauling strategy is insufficient to guarantee the minimum power consumption and the required data rates. We formulate an optimization problem that considers the estimated hourly traffic load and determines the most energy efficient backhauling strategy for various hours of the day. Considering the complexity of the optimization problem, we also propose an energy efficient heuristic solution to solve this problem. Simulation results indicate that the proposed solution provides up to 32% more energy savings than the existing solution.

Existing System

In the exisring system we investigate the green backhauling challenge for a fifth generation (5G) wireless communication network that uses both the passive optical network (PON) and millimeter wave (mmWave) backhauling to support its diverse groups of customers and applications. Our approach is based on the fact that the energy efficiency figures for the PON and the mmWave technologies are different under a given load condition

Disadvantages in Existing System

- Energy dissipations in lightly Loaded systems

Proposed System

In our Proposed work, we will further investigate this along with other energy-saving mechanisms (e.g.,sleep mode for lightly loaded RRUs) for C-RANs.The proposed work is most advantageous since the lightly loaded system reduce the power wastages.

Advantages in Proposed System

- Programmable Mode of operation to save Energy

Software Used

MATLAB 2013a